## Slide 1: QuickDough: A Rapid FPGA Loop Accelerator Design Framework Using Soft CGRA Overlay
Cheng Liu, Ho-Cheung Ng, Hayden K. H. So
Department of Electrical and Electronic Engineering University of Hong Kong
FPT 2015 – 2015/12/07

## Slide 2: Background: Hardware Accelerators
Numerous successful demonstrations using CPU + Hardware Accelerator.
  CPU control intensive,
  Hardware Accel. parallel compute intensive kernels
FPGA Accel. vs. PHI Accel. vs. GPU Accel.
  FPGA Accel.: long history, energy efficient, low latency, many successful examples but limited adoption.
  PHI & GPU Accel.: short history, 5 of the top10 super computers use PHI or GPU.

## Slide 3: Background: Why not FPGA Accelerator?
Low design productivity of designers!
  Low-level abstraction level
  Lack of run-time and compilation-time support
  Lack of efficient implementation and debugging
FPGA Accel. Development
HLL
HDL
Bitstream
Debug
Final Design
Debug
Compile-debug-edit cycle
Up to hours
or days!
Edit
Edit
Notes: Explain what do you want to say with the animation. I guess you want to say users will do 2 levels of design iterations, one in HDL design and one in implementation. And you want to argue that implementation is part of the bottleneck for design iterations, correct?
Yes, I want to make it clear that this work helps to decrease the edit-compile-debug cycle. While debug may also happen in simulation stage where implementation is not needed at all. This work will particularly be useful in a in system debugging scenario where you need to download the FPGA bitstream and debug it in a run-time system. Also we agreed that this work focuses on the implementation instead of the rest two design productivity challenge.

## Slide 4: Background: Overlay Architectures
User Application
Netlist
C/C++/Java/…
HDL
Virtual FPGA
GPU
CGRA
Vector Processor
RAM
LUT
DSPs
FFs
Processors
Overlay
FPGA
Application Mapping
Overlay Mapping
Benefits
  Larger resource consumption
  Possible performance degradation
Challenges
  Higher abstraction level
  Virtualization  better portability
  Improved debugging capability
  Separation of HW/SW concern
Notes: Remove the confusing part and make this slide focusing on general overlay advantages and disadvanatges

## Slide 5: QuickDough Overview
A high productivity compilation framework for high-level applications on CPU-FPGA computers.
  Compiles software and FPGA accelerator design within the same framework
  Overall SW-like compile speed
  Increase # of debug-cycle-per-day
  Promising performance speedup

## Slide 6: QuickDough Design Flow
Fast and common route
Slow yet less frequent route
Optimization for
performance/
power/
energy efficiency

## Slide 7: QuickDough Soft CGRA Overlay
Highly pipelined, good scalability, simple and easy to extend

## Slide 8: Loop Execution on the Accelerator

## Slide 9: Accelerator Selection
DFG
CGRA Size
Impl. Freq.
I/O Buffer
I/O Address Buffer
Data Mem
Inst. Mem
Operation
Scheduling
# of cycles
Of DFG execution
Loop
computing time
Loop data
transmission time
Analyze
Group Size
Loop
DMA
Model
Loop performance
Minimum data
mem, inst. mem
requirements.
Accel.
Config.
Communication
drivers
Config.
filter
Most time-
consuming
Potential
Config.
Optimized
Config.
Notes: It is somewhat too detailed in this slide, but it helps to explain the trick that operation scheduling can be reused for multiple accelerator configuration selection. Different parameters of the accelerator configuration are estimated in a different way. Basically, instead of evaluating each configuration sequentially, the selection process starts with the operation scheduling which requires DFG and CGRA size as input. With the operation scheduling, the performance of a group of accelerator configurations can be obtained with modeling. The rest of the design parameters can be evaluated.

## Slide 10: Accelerator Selection
Selection Strategy
  -O0: accelerators with smallest CGRA size
  -O1: target three groups of accelerators with different SCGRA size (small, medium, large)
  -O2: full search
A single operation
scheduling can be reused
to evaluate a group of
accelerator configurations.
Accelerator library
CGRA
Size
2x2
CGRA
Size
5x5

## Slide 11: Accelerator Library Pre-build

## Slide 12: Benchmark
Benchmark | App Parameters | Loop kernel
MM (Matrix multiplication) | matrix size: 100100 | 100
FIR | # of input: 10000 # of Taps +1: 50 | 0
SE (Sobel edge detector) | # of vertical pixels:128 # of horizontal pixels: 128 | 
KM (Kmean) | # of nodes: 5000 # of centroids: 4 # of node dimension: 2 | 
Benchmark | App Parameters | Loop kernel
MM (Matrix multiplication) |  | 
FIR | # of input: 10000 # of Taps +1: 50 | 
SE (Sobel edge detector) | # of vertical pixels:128 # of horizontal pixels: 128 | 
KM (Kmean) | # of nodes: 5000 # of centroids: 4 # of node dimension: 2 | 
Benchmark | Unrolling | DFG Size
MM | 1100 | 
FIR | 5050 | 200
SE | 163 | 
KM | 2 | 
Benchmark | Unrolling | DFG Size
MM |  | 
FIR |  | 
SE |  | 
KM |  | 

## Slide 13: Common Operations of the Benchmark
Type | Opcode | Expression
MULADD | 0001 | Dst = Src0 x Src1 + Src2
MULSUB | 0010 | Dst = Src0 x Src1 - Src2
ADDADD | 0011 | Dst = Src0 + Src1 + Src2
ADDSUB | 0100 | Dst = Src0 + Src1 - Src2
SUBSUB | 0101 | Dst = Src0 - Src1 - Src2
PHI | 0110 | Dst = Src0 ? Src1 : Src2
RSFAND | 0111 | Dst = (Src0 >> Src1) & Src2
LSFADD | 1000 | Dst = (Src0 << Src1) + Src2
ABS | 1001 | Dst = ABS(Src0)
GT | 1010 | Dst = (Src0 > Src1) ? 1 : 0
LET | 1011 | Dst = (Src0 <= Src1)? 1 : 0
ANDAND | 1100 | Dst = (Src0 & Src1) & Src2

## Slide 14: Experiment Setup
SCGRA Topology | 2D Torus
Instruction Memory Data Width | 72 bits
Data Memory | 256 x 32 bits
I/O Buffer Data Width | 32 bits
I/O Addr Buffer Data Width | 18 bits
Basic SCGRA Configurations
DMA Size | ≥512 | 256 | 128 | 64 | 32 | 16 | ≤8
Latency/Word (ns) | 10.08 | 11.28 | 13.32 | 15.18 | 21.45 | 36.24 | 63.00
DMA Latency
Notes: DMA latency is needed to estimate the communication cost of the loop which are part of the loop performance

## Slide 15: Accelerator Library Pre-build
Notes: When the user provides the BRAM resource budget, we use it to decide the size of the pre-built accelerator library. Apparently, the larger budget is provided, the more accelerators need to be pre-built. And it will take longer time to pre-build the library. Thus this figure present the cost of the library pre-building process. The blue line shows how the number of accelerators increases with the BRAM budget. While the red line shows the how the library pre-building time changes with the BRAM budget.
There are 140 RAMB 36 on Zedboard and I want to use it as a reference of the BRAM Budget.

## Slide 16: Resulting Accelerator Configurations
Opt. Option | Resulting Config | MM | FIR | SE | KM
O0 | SCGRA size | 2x2 | 2x2 | 2x2 | 2x2
 | Inst. Mem Depth | 4K | 4K | 4K | 4K
 | I/O Buffer Depth | 4K | 4K | 4K | 4K
 | Grouping Factor | 50x5x100 | 2500x50 | 128x64x3x3 | 1250x4x2
O1 | SCGRA Size | 3x3 | 3x3 | 3x3 | 5x5
 | Inst. Mem Depth | 2K | 2K | 4K | 1K
 | I/O Buffer Depth | 2K | 2K | 1K | 2K
 | Grouping Factor | 25x5x100 | 1250x50 | 64x32x3x3 | 1000x4x2
O2 | SCGRA size | 3x3 | 4x4 | 4x4 | 5x5
 | Inst. Mem Depth | 2K | 1K | 2K | 1K
 | I/O Buffer Depth | 2K | 8K | 1K | 2K
 | Grouping Factor | 25x5x100 | 5000x50 | 64x32x3x3 | 1000x4x2
Notes: The table seems to be to large to put it here. Any suggestions for this one?

## Slide 17: Accelerator Generation Time

## Slide 18: Accelerator Performance

## Slide 19: Accelerator Performance

## Slide 20: Accelerator Implementation
Notes: Yes, as you mentioned, there is actually nothing significant to highlight in terms of implementation. I thought implementation is part of the experiment and completes this section. Anyway, one thing that may be worth mentioning is the fmax remains very good when the BRAM utilization is very high.

## Slide 21: Conclusion
By using an SCGRA overlay, a rapid FPGA loop accelerator design framework is proposed.
  With a pre-built SCGRA overlay based accelerator library, FPGA loop accelerator can be generated in seconds.
  A highly pipelined CGRA overlay template is developed to ensure the performance of the resulting accelerators.
  The accelerator communication interfaces are also generated forming a HW/SW co-design framework accessible to software designers.

## Slide 22
Thank you very much!